## Slide 1
Devices for burning biomass

## Slide 4: BIOMASS BURNING DEVICES
Cast iron head sets
Ceramic head sets
Cast iron head feeder
Ceramic head feeder

## Slide 5: BURNERS’ POWERS
Cast iron head
Features a movable step grate and a multi point air inlet system
20 KW
30 KW
40 KW
60 KW
120 KW
180 KW
240 KW
FUEL HUMIDITY UP TO 25%
CERAMIC HEAD
Made from high temperaturę resistant materials (approx. 1100C), features a multi point air inlet system and an ash removal system
30 KW
50 KW
100 KW
240 KW
FUEL HIMIDITY FROM 25% UP TO 40%

## Slide 6: FUEL CONTAINERS
VOLUME
0,6 m3
1,0 m3
2,0 m3
4,0 m3
6,0 m3
8,0 m3
10,0m3
27,0 m3
CONTAINERS 0,6 m3 -2m3 – 230V (up to 120kw)
CONTAINERS 4 m3 -27m3 – 400V
.

## Slide 7: ALTERNATIVE TO CONTAINERS: SPRING FEEDERS

## Slide 8: SPRING FEEDERS ELEMENTS:
1 – mounting plate, 2 – shield, 3 – spring raking arms, 4 – base, 5– conveyor/feeder, 6 – motoreducer

## Slide 9: Chamber conveyor (ROTARY FEEDER)
1 – lower feeder screw, 2 – lower feeder cover, 3 – driving motoreducer, 4 – chain gear, 5 – clutch, 6 – dosing feeder cover, 7 – dosing feeder rotor, 8 – mounting base – Belimo system (moving grates), 9 – feeder temperature sensor duct

## Slide 10: CAST IRON BURNER
1 – movable grate, 2 – fixed grate, 3 – head fireplace, 4 – burner cover, 5 – grates driving motor, 6 – fan, 7 – burner cleaning opening

## Slide 11: Motoreducers
240V | 0,6 – 2М3 CONTAINERS | SPIRAL BEVEL GEAR(1/60, 0,75 kW 900 rpm) | 
380V | 0,6 – 2М3 CONTAINERS | Cylindrical bevel gear 1/125, 0,75 kW 1400 rpm | 
380V | 4,6,8,10М3 CONTAINERS | UPPER FEEDER – CYLINDRICAL GEAR 1/100, 1,5 KW 1400 rpm LOWER FEEDER – CYLINDRICAL GEAR 1/100, 0,75 KW 1400 rpm | 
380V | SPRING ARMS | UPPER FEEDER – CYLINDRICAL BEVEL GEAR 1/120, 1,1 kW 1400 rpm LOWER FEEDER – CYLINDRICAL GEAR 1/100, 0,75 KW 1400 rpm | 

## Slide 12: TYPES OF FUEL
The „SMOK” is intended for burning various types of biomass in the form of sawdust, chips, shavings, briquette, pellets or grains and fruit pits
Р45 chips
SAWDUST
BARK
BRIQUETTE / AGRO-BRIQUETTE
PELLETS/ AGRO – PELLETS
Processed and unprocessed fuels

## Slide 13: QUALITY OF BIOMASS. NORMS, PROPERTIES, REQUIREMENTS
EUROPEAN NORM
CEN/TS 14961
Fraction size (P16/P45/P63/P1000)
Moisture content (М20/M30/M40/M55/M65)
ash(A0.7/A1.5/A3.0/A6.0/A10.0)
Heating value MJ/kg
density, kg/m3
Сhlorine contant ,%
Nitrogen contant,%
COUNTRY SPECIFIC NORM
ONORM M 7135 AUSTRIA
SS 187120 SWEDEN
DIN 51731 GERMANY
CTI – R 04/5 ITALY
BRITISH BioGen ENGLAND

## Slide 14: WOOD CHIPSACCORDING TO NORM Р 45
Main fraction˃80%
3.15≤ P ≤ 45 mm
Fine fraction ˂5%-m
˂1mm
Coarse fraction,
Max. Particle length˂1 m - %˃63 mm

## Slide 15: WOOD CHIPS ACCORDING TO NORM Р 45
Main fraction˃80%-m
3.15≤ P ≤ 45 mm
Fine fraction ˂5%-m
1≤P≤3,15mm
Fine fraction 5w-%˂1 mm
Coarse fracation,
Max. Particle length ˂1 m - %˃63 mm

## Slide 16: Wood briquette
origin– barkless wood, not chemically treated
Moisture content– М10
Particle density– DE1.0 (1.00-1.09 kg/dm3)
Ash content: A 0.7 %
additives ˂2 %
Net heating value E4.7 (E≥4,7kWh/kg = 16,9 MJ/kg)
Briquet with bulk density up to 450kg/m3

## Slide 17: PELLET
origin– barkless wood, not chemically treated
Moisture content– М10
Mechanical durability DU97,5 (97.5 w-% of granulate in 100 g should not be crushed in testing)
% dust content
Ash content A 0.7 %
Sulphur content
additives ˂2 %
Net heating value E4.7 (E≥4,7kWh/kg = 16,9 MJ/kg)

## Slide 18: Heating price comparison
 | electricity Two-rate electricity (50/50%) Liquid petroleum gas mazut Electricity, 2nd rate District heating Natural gas Coke Coal Heat pump E=4 (daily rate) Heat pump E=4 two-rate (50/50%) Heat pump E=4 (2nd rate). Biomass.

## Slide 19: SMOK schematics
AZSB GZ 30R 1M3 Z SUP (230V)
AZSB 30 GC 6M3 P SUP

## Slide 20: SMOK Schematics
APSB 50 GC 2M3 P
APSB 240 GZ 6M3

## Slide 21: SMOK schematics, configuration
APSB GZ 240N NS1604

## Slide 22: APSBGZ120R NS1243

## Slide 23: APSBGZ120R NS1244

## Slide 24
SMOK – IRELAND AZSB GZ 240 KW NS

## Slide 32: SLOVENIA

## Slide 33: POLAND
PL - CHWALISZEWO
23 YEARS OF OPERATION